Comptia A+ Study guide
Comptia A+ Cert. 1001

Section 2 Notes
Chapter 1 – Safety and Professionalism
- Tools of the trade
  - You can buy PC repair tool kits.
  - There are kits for mobile devices.
  - Use a voltage tester or volt-ohm meter to test input voltage.
  - Always carry multiple thumb drives.
- Troubleshooting theory
  - The system unit provides processing and storage.
  - Common input devices include keyboards, mice, and scanners.
  - Common output devices include monitors, printers, and speakers.
    - Step 1: Identify the problem
    - Step 2: Establish a theory to determine cause
    - Step 3: Test the theory to determine cause
    - Step 4: Establish a plan of action to resolve the problem and implement the solution
    - Step 5: Verify the full system functionality and, if applicable, implemnt preventative measures.
    - Step 6: document finding, actions, and outcome.
- Section 3 Notes
  Chapter 2: the visible computer
- The system unit contains the motherboard, CPU, RAM and hard drives; everything other device is a peripheral.
- Monitors and web cameras provide visual output.
- Keyboards, mice, and game controllers provide input.
- Printers create paper output.
- Speakers and headsets make audio output.
  External Connections
- Make sure you can recognize all the rear desktop connections, including USB, network, power, video, and audio.
- Be familiar with common front desktop connections.
- Make sure you can identify common connections on laptops.
  Inside The PC
- Recognize the position and shape of power supplies and video cards.
- Be familiar with the parts of the motherboard.
- Make sure you can recognize the function of core components : RAM sticks, CPU, M.2 SSDs, and hard drives.
- Understand the function of expansion slots.
  What is a Computer?
- A computer gets work or play done.
- A computer will have a CPU, RAM, mass storage, and an operating system.
- Laptops, mobile devices, and the internet of things (IoT) devices are all computers.
  Section 4 Notes
  Chapter 3: CPU’s
  What is a CPU?
- Central processing units run programs.
- Every CPU has internal features to process commands.
- Every CPU runs code based on a specific machine language.
- CPU’s use pipelines to optimize the processing commands.
  CPUs cores and Speeds
- CPUs have a clock speed, commonly measured in GHz (billions of cycles/sec)
- CPUs come in primarily two makes Intel and AMD
- CPUs take a system speed and multiply it to reach the Max CPU speed.
- Single CPUs often have multiple cores.
  Caching
- CPU caching works between RAM and the CPU
- Cache is built into the CPU
- It’s common to have three caches in a CPU: L1, L2, and L3
CPU Sockets
- CPU sockets are the mount where a CPU connects to the motherboard.
- CPUs micro-architectures
- Many different CPUs come from a single micro-architecture.
- There are specific CPU socket packages covered on the A+.
- LGA 1151 – Mainstream type socket. Lot of middle of the road CPU’s have this and some others as we go moving into the enthusiast side.
- LGA 2066 – Enthusiast world. Higher CPUs use this socket (I9’s etc)
- AM4 – Neck and neck with LGA 1151 in terms of mainstream and being slightly on the enthusiast side.
- TR4 – Used on enthusiast and high end work stations today.
  Installing a CPU
- Makre sure you have the right socket and speed CPU for your motherboard.
- Always use thermal paste between the CPU and the fan.
- Connect the fan to a power source.
  Liquid Cooling
- Third party fans are often more efficient than OEM fans.
- Liquid cooling uses a pump, a radiator and a cooling block with liquid to remove heat.
- Liquid cooling reduces fan noise.
Section 5 Notes
Chapter 5: RAM
Ram Technology
- Different motherboards support a specific RAM technology.
- The technologies on the comptia a+ are DDR, DDR2, DDR3 and DDR4.
- We measure RAM speeds using DDR or PC ratings.
- Multiply a DDR speed by eight to get the PC speed.
  Ram Capacity
- Every stick of RAM has a specific capacity.
- RAM comes in single- and double-sided versions
- Motherboards offer multichannel memory
- RAM should be identical in the same channel.
  Ram Features
- SO-DiMM – For smaller form factors where long ram sticks wont fit.
  - Just cause they are SO-DIMM everything else said about ram remains unchanged. Simply a smaller form of ram.
- SPD – Chip allows you to query RAM
  - CPU-Z has SPD settings that allow you to take advantage of this type of RAM.
- Parity and ECC RAM contain extra chips to check for RAM errors.
- ECC RAM is only for motherboards that support it.
- SO-DIMMS are for smaller spaces
- Almost all RAM has SPD chip that stores information about the RAM stick.
- Tools like CPU-Z read SPD information.
  Installing RAM
- Use the motherboard book to make sure you’re installing the right RAM capacity and speed.
- Line up the notch and drop the RAM straight into the slot.
- Watch when the system boots to verify the system sees the installed RAM
- Make sure RAM is fully installed and channels are properly filled.
  RAM Quiz
- DDR4 RAM modules have how many pins?
  - DDR4 RAM modules have 288 pins.
- Which type of RAM modules have 240 pins?
  - DDR2 and DDR3 RAM modules have 240 pins
- Which technology makes simultaneous access to multiple RAM modules?
  - Dual channel memory provides simultaneous access to two RAM modules when reading or writing. Synchronous RAM is technology that keeps RAM timing matched to the system clock. Single and double-sided RAM modules are configurations that determine the capacity of RAM modules.
- Which RAM would typically be installed into a laptop computer?
- Laptops and other small form factor motherboards typically use SO-DIMM memory modules. ECC RAM is usually found in server-grade computers. SDRAM is an early generation of RAM technology but it is not specific to laptop. There is no such thing as SPD RAM.
- What types of RAM can function even if one of the memory chips fail?
  - ECC RAM and Parity RAM can function with a failed memory chip. SO-DIMMs are small outline (form factor) memory modules. Dual-channel is technology that supports simultaneous access to multiple RAM modules. Double-sided RAM are RAM modules that are organized into 4-bits.
- In what order should memory slots be populated?
  - Memory slots should be populated according to the instructions in the motherboard manual
  Section 6 Notes
  Chapter 5: Firmware
  What is a BIOS?
- BIOS is programming. It is code burned to a chip.
  - Not software (burnt to magnetic media)
- Power-On Self- Test (POST)
- System Setup (CMOS)
- BIOS programming enables interation with motherboard before OS loads.
- BIOS is stored in nonvolatile media, thus called firmware.
- POST routines are built intro firmware.
- The System Setup utility is also part of the firmware.
  POST
- CPU’s power good wire receives voltage, talks to the BIOS, and runs Power On Self Test (POST).
  - POST is a call to all PC components to run internal diagnostics and report results back.
  - When a POST finishes successfully you will hear one beep upon start up.
  - Depending on what reports back as not running correctly there are several beep codes.
- POST runs at boot, requesting devices to self check.
- POST errors manifest as specific beep codes or display (text) codes.
- POST cards enable testing of “dead” computers.
  System Setup
- Unified Extensible Firmware Interface (UEFI).
  - UEFI replaces traditional 16-bit BIOS in modern systems.
- The System Setup enables custom information about changeable devices.
- System Setup enables changes to CPU frequencies, RAM timings, BIOS passwords, boot option, and more.
  Troubleshooting firmware
- Complementary metal-oxide-semiconductor (CMOS).
  - Back then if changes were made to BIOS through System Settings it was saved in tiny CMOS chip (very small space, 64K etc).
- Single Flash ROM chips (Flash Memory)
  - Today this is the type of BIOS that is commonly seen.
  - Flash ROM can be flashed if BIOS is to be updated.
- Real-Time Clock (RTC)
- CMOS Battery
  - Every motherboard has a built in battery.
  - Say you have multiple computers synchronized to a certain time and they are completely disconnected from a power source CMOS battery continues to keep track of time.
  - If you don’t have a great battery your time will slow down. (Ex. Computer is 20 minutes behind from other computers, could be a sign of failing CMOS
  - battery).
- Flashing the ROM updates the firmware on flash chip.
  - Make sure you have good power. You cannot lose power during this step. Can ruin motherboard. (UPS is a good recommendation).
  - BIOS flash image. Big reason for updating BIOS is for motherboard to handle new CPU’s.
  - One way is to copy BIOS flash image to thumb drive and connect to PC and select file though system settings. New motherboards have an option to go through the internet directly.
  - Make sure you have a good reason to want to upgrade BIOS. It is a risky procedure so make sure it is worth it.
- The real-time clock battery keep system time without external power.
- System Setup allows for changes; exit without saving is an option.
- Reset Sytem Setup for defaults.
- Flash the ROM chip to update firmware.

Firmware Quiz
- BIOS programs that enable hardware to function are called what?
  - Services are BIOS programs that make hardware functional. POST is a testing program in BIOS. CMOS is a type of memory chip. Device drivers make hardware function in an operating system.
- Which is found in BIOS?
  - The Power On Self Test (POST) program and the services are contained in the BIOS chip. The CMOS battery is not inside a chip. The RTC is in the CMOS chip, not the BIOS chip. The explanation of POST hex codes can be found in the system manual.
- What is the primary purpose of POST?
  - POST is a program in the computer's BIOS chip that performs diagnostics prior to the computer booting an operating system. POST can send messages to a POST card but the card does not contain the POST program. A power supply provides power to the CPU. POST does not enable hardware, it tests hardware.
- For which failures would you expect POST to issue beep codes?
  - Beep codes are issued when error messages can't be displayed on the screen. A bad video card would cause beep codes. Missing keyboard, printers, and network connection failures can be shown on a screen. The POST program will not run at all without a CPU installed (and thus would not generate a beep code).
- How would a technician start the system setup program?
  - Every computer has a certain key on the keyboard that must be pressed before the OS boots to launch the setup program. There is no automatic procedure or button to start the setup program. The administrator password is not entered until after the setup program has started.
- To prevent random people from booting the OS, a technician should do what?
  - A user password prevents the OS from booting until the password is entered. The administrator password prevents access to the setup program until the password is entered. Flashing the BIOS is for fixing bugs and adding features to the contents of the BIOS chip. Removing the CMOS battery might prevent the OS from booting, but it is not the best answer.
- Which is more likely to cause a computer's reported time to fall behind?
  - A weak or failed CMOS battery will slow the system clock and may cause other problems. Missing a leap year won't affect the computer's clock rate. Low wall voltage is adjusted in the power supply; if it is too low, the computer won't boot.
- Which battery provides power to the RTC and CMOS chip?
  - CR2032 is the standard CMOS battery. The other choices are not normally used for CMOS in a computer.

Section 7 Notes
Chapter 6: Motherboards
Form Factors
- Motherboards and cases follow standardized form factors.
- Common form factors: ATX, microATX, Mini-ITX.
- Power supplies offer standardized connectors.\
  Chipsets
- Chipsets combine functions from many single-function chips
- Early chipsets offered Northbridge and Southbridge
- Modern chipsets feature Southbridge(CPU handles Northbridge functions).
- Chipsets define RAM capacity, USB capabilities, and much more.
  Touring the Motherboard
- The motherboard manual provides essential setup information.
- Motherboards come with cables, standard connectors, and more.
- PCIe is the most common expansion bus, it offers multiple lanes.
- Motherboard is riddled with voltage regulator modules and capacitors to adjust voltages.
  - Power supplies provide 12V, 5V and 3.3V to the system. System then breaks down those 3 voltages into hundreds of different voltages.
  - Capacitors would adjust 3.3V to 1.3V for one pin, 2.1V for another etc.
  Touring The Case
- Cases offer standardized standouts for mounting various motherboard form factors.
- Better cases offer cable management features.
- Pick a case that has support for number and type of drives needed.
  Installing a motherboard
- Install and test CPU and RAM on motherboard before putting in case.
- Install I/O shield and triple check standoff positions.
- Mount motherboard and connect motherboard cables.
- Use the motherboard manual if necessary.
  Motherboard Quiz
- The largest motherboard form factor is?
  - In order of largest to smallest, the form factors are ATX, Micro-ATX, ITX, and Mini-ITX.
- Which is true of an I/O shield?
  - I/O shields are customized to fit the motherboard I/O area. I/O shields have standard dimensions to fit standard form factor cases. Micro-ATX motherboards are 9.6x9.6, not their I/O shields. Different motherboards have different I/O ports so it is impossible to create a one-size-fits-all I/O shield for different motherboards.
- Which chip is typically found on modern motherboards?
  - The South Bridge is typically found on modern motherboards. The functions of the old North Bridge chip have been moved onto modern CPUs. The CMOS battery is mounted on the motherboard, but it is not a chip, it is a battery. Second bridge is a made-up term.
- The job of the South Bridge is to act as the interface between the CPU and what?
  - The South Bridge interfaces slow hardware such as hard drives and keyboards to the CPU. The CPU interacts directly with fast hardware including RAM and video cards.
- Which is typically not found on a motherboard?
  - SATA cables attach to connectors on the motherboard, but they are not part of the motherboard. PCIe slots, voltage regulators and power connectors are all found on motherboards.
- Connectors with cables that plug into the motherboard are known as what?
  - Cable-connected ports are dongles. Dangles is not a computer term. Slots are for plugging in RAM and expansion cards. The I/O shield does not connect to the motherboard.
- Keeping the wires in a case neat, out of the way and easy to identify is called what?
  - Cable management is the technique of organizing cables inside a case.  Pass throughs are holes in the chassis that help facilitate cable management.  There are no cable bays in a computer case. Structured cabling describes the organization of large, well-designed network cabling installations.
- Which critical components are found on the outside of the case?
  - Front panel connections are placed on the outside of the case. Power supplies, hard drives and SSDs are typically found inside the case. Tower cases are a type of case, not a component found inside or outside of one.
- Which is it best to do before mounting the motherboard in the case?​
- The best answer is to test the motherboard with a CPU and RAM installed. It is harder to install a CPU and RAM once the motherboard is mounted so removing them is not a good idea. It may be possible to connect cables to the motherboard before installing it into the case but it makes the installation challenging.
- Which must be done before installing a motherboard into a case?
  - The I/O shield must be installed before the motherboard is installed; it won't fit after the board is in place. Case fans and SATA cables can be installed at any time. Installing a video card into the motherboard may make it challenging or impossible to install the motherboard into the case.
  Section 8 Notes
  Chapter 7: Power Supplies
  The Power Supply
- Provides 12V, 5V, and 3.3V.
- Power supplies transform AC from wall outlet to DC for the computer.
- Standard connectors for motherboard are 20-24 pin ATX and 4-8 pin P4
- Use Molex and SATA connectors for peripherals and drives.
  Mounting The Power Supply
- Mount the power supply in the PC case with four screws.
- Orient the power supply so fans draw air from system
- Connect motherboard primary and secondary power
- Modular PSUs offer less cable clutter than non-modular PSUs.
  Choosing a Power Supply
- Volts x Amps = Watts.
- Get a PSU with a little more wattage than your system needs
- Shop for higher- efficiency power supplies.
- Modular power supplies cut down on cable clutter.
  Cooling your PC
- Overheat = Reboot.
- 4 pin CPU fan connectors are better known as PWM connectors.
- A heat sink draws heat from electrical components.
- Fans blow heated air through and out of the system.
- Fan speed and noise can be controlled through firmware or software.
  Troubleshooting Power Supplies
- Best way to troubleshoot a power supply is to test it.
  - They have useful power supplies testers which tell you how much voltage is coming from all the connections.
- Multi-meter V with squiggle = AC.
- Multi-meter V with line and three dots = DC.
- Power supplies die fast with burning smell, smoke, or both.
- Power supplies die slowly and cause intermittent problems.
- Use PSUs tester or multi-meter to test power supplies.
  Troubleshooting Core Components
- If you have a booting system and through messing with the system settings it is unbootable (or user password is unknown) consider setting off the CMOS jumper.
  - CMOS jumper erases ass system settings and reverts to defaults.
  - Incorrectly installed CPUs or RAM can make it seem like your PC is dead.
  - Install core components and test before mounting into the case.
  - Errors in System Setup can cause a dead PC; try clearing the CMOS jumper.
  - Windows offers memory diagnostic tools to help with potentially bad RAM.
  Power Supply Quiz
- A power supply with optional cable plug-ins is known as a what?
  - A modular power supply simplifies cable management by enabling you to add and remove optional plug-in cables as needed to power components. Option power supply is a made-up term. A Flex power supply is a small-form-factor power supply. A soldered power supply has all of its power cables soldered to the power supply unit (PSU).
- What does the on/off switch on a power supply do?
  - It allows power to flow from the plug into the power supply. The computer has its own on/off switch. The power supply powers the "power good" wire (if the power is good) but the power supply switch does not do this directly. Power supplies (mostly) do not autodetect power and then react.
- The four/six/eight pin connector (known as the P4 connector) on the ATX 12V power supply provides power to which computer component(s)?
  - The ATX 12V power connectors send power to the CPU. The other devices get power from the main power connector.
- Which is a primary characteristic to be considered when choosing a power supply?
  - Efficiency is a major consideration. Cable length is important, but most power cables are of sufficient length and don't typically need to be measured or checked. Power supplies do not have a sag rating. UPS compatibility is not a real specification.
- Which is the quietest cooling solution?
  - Liquid cooling is the quietest solution. Fan noise varies depending on size and speed, but small fans (which have to spin faster to move the same amount of air) tend to be louder than large ones. SpeedFan is a fan controller program, not a cooling solution.
- What is the primary result of overheating the CPU?
  - CPU overheating causes shutdowns and reboots. Overheating does not increase or decrease performance. Overheating does not cause fans to spin faster.
- The voltages output by a PSU can be checked with which tool?
  - A power supply tester checks the voltage of each wire. Using a finger can injure you and it isn't calibrated to give an accurate reading. A paper clip cannot test voltage. If you get a positive result from using a smoke detector to test a power supply, you need to grab a fire extinguisher!
- Catastrophic (fast) power failures typically include which symptom?
  - Catastrophic power supply failure may be accompanied by a burning odor. A catastrophically-failed power supply is dead; it cannot provide enough power for slow performance or rebooting. Power supply voltage decay over time is a symptom of a slowly failing power supply.
- Unexpected noise coming from inside a running computer likely comes from what?
- Cables or loose items in a case that contact spinning fan blades causes unpleasant and unexpected noise. Failing RAM only generates beep codes during the POST process at boot up. Failing speakers and overheated CPUs don't usually make noise.
- If installed RAM does not show up in the CMOS setup program, what is the best course of action?
  - Re-seat the RAM. None of the other choices will cause the system to recognize previously unrecognized RAM.
  Section 9 Notes
  Chapter 8: Mass Storage Technologies
  Introduction to Mass Storage
- There are many types of mass storage used today, including hard drives, solid state drives, and optical media.
- Regardless of the media your operating system sees mass storage as a string of logical block addresses.
- There is a difference between decimal values and IEC values.
  Magnetic Disk Drives
- Advanced Technology Attachment (ATA)
  - Language of hard drives/Magnetic disk drives.
- Parallel ATA (PATA)
  - Long dead, not on comptia exam anymore. Won’t see this unless you are working on a really old computer.
- What we see today is Serial ATA (SATA)
- eSATA – Sata connection, but used externally.
  - With advancements in USB eSATA is not as popular as it once was.
  - Adding a eSATA expansion card to a system makes it easier to use eSATA devices. On more modern motherboards.
- Magnetic disk drives use spinning platters to store data via magnetism and read/write heads.
- Hard disk drives come in 3.5”, 2.5”, and 1.8” physical sizes.
- We use the Advanced Technology Attachment protocol to communicate with hard disk drives.
- The dominant ATA is called Serial ATA (SATA).
  Solid State Drives
- Memory is broken down into blocks, pages contain blocks. A single chip may contain hundreds to thousands of pages.
- Come in a number of sizes.
  - Most common is 2.5”.
  - M.2 SSD is also common in modern systems.
- SSD’s are much faster than HDD’s.
- Non-Volatile Memory Express (NVMe).
  - Manifest usually as M.2. Much faster than SATA.
  - Solid state drives (SSD’s) store data using chips; tehre are no moving parts.
  - Data is stored in blocks and pages.
  - SSD’s come in traditional 3.5” and 2.5” sizes, but also come in M.2 format.
  - Some SSD’s use the very fast NVMe protocol instead of SATA for increased performance.

SCSI
- Parallel ATA – A bunch of parallel wires talking to each other a the same time. Outdated for the most part and only seen on old machines.
- Small Computer System Interface (iSCSI)
  - SCSI devices connected via ethernet cables.
  - Developed around the same time as ATA. Competing languages.
- Serial Attached SCSI (SAS)
- The Small Computer Systems Interface (SCSI) is an ancient standard that still has great support.
- The old parallel SCSI is long gone, but the SCSI language lives on in serial SCSI versions.
- Two modern SCSI standards are SAS (Serial Attached SCSI) and iSCSI.
  Boot Order
- When a system boots, it looks for a bootable device.
- It’s important to make sure the system looks for correct boot devices.
- The boot order is defined in the CMOS system setup.
  Mass Storage technologies Quiz
- Mass storage is organized into __________?
  - Storage is organized into Logical Blocks (LBAs). Gigabytes and Gibibytes describe capacity, not organizational structure. Pages are the organizational structure of SSDs but not of all mass storage devices.
- Which does not describe a mass storage device?
  - An M.1 drive is not a mass storage device; it is a made-up term that closely resembles the M.2 form factor. Optical drives, magnetic drives and SSDs are all mass storage.
- Which is a standard command and connection standard for mass storage devices?
  - Advanced Technology Attachment (ATA) is a command and connection standard for mass storage devices. Form factors are not command or connection standards. LBA is an organization structure for mass storage devices.
- Using SATA, how is data passed between the computer and hard drive?
  - SATA uses a serial data transfer protocol. Data is transferred one bit at a time from the drive to the computer and one bit at a time from the computer to the drive. SATA does not pass data 2-bits, 4-bits or 8-bits at a time.
- SSDs are organized into logical blocks, but their memory storage cells are called what?
  - SSD memory cells are called pages. Magnetic drive storage units are called sectors. Slots and sockets are not terms to describe storage units.
- Which interface is the fastest?
  - NVMe uses PCIe lanes and is the fastest of these interface choices. PATA is the slowest; SATA and SCSI speeds fall between NVMe and PATA.
- Combine SCSI with SATA to get ____________?
  - Serial Attached SCSI (SAS) uses the SATA connector with the SCSI command language. M.2 is a connector interface and form factor. SSCSI and SASI are made up terms.
- Running SCSI commands over Ethernet is called __________?
  - iSCSI uses SCSI commands sent over Ethernet. SCSIi, eSCSI, and SCSIe are made up terms.
- Which cannot be set as the first boot choice?
- UEFI is a firmware interface, not a boot device. Any of the other choices can be set as a boot device.
- Which is a likely reason for a computer to fail to boot?
  - A computer cannot boot from a non-bootable device or media. USB drives, optical drives, and SSDs and are all valid boot devices (but will only boot if they contain a working, properly-created bootable drive image).
  Section 10 Notes
  Chapter 9: Implementing Mass Storage
  New installation – First Drive
- The first drive on a system relies on the OS install program to provide partition and format functions.
- The partitioning and formatting tools in installation programs provide a subset of tools when compared with their main tools.
- Installation tools may provide features not normally seen anywhere else (such as swap file creation).
  RAID
- RAID 0 – Striping. Piece of document is shared between 2 hard drives. If one hard drive fails all data is lost essentially as you are missing important pieces of said document.
- RAID 1 - Mirroring. Copy of document is saved on both drives. Safer data storage essentially although it is rather redundant.
- RAID provides speed and/or redundancy.
- RAID 0 (striping) provides speed.
- RAID 1 (mirroring) provides redundancy.
- RAID 5 and 6 (Striping with parity) provides speed and redundancy.
- RAID 5 can only lose one drive in the array; RAID 6 can lose two.
  Hardware RAID
- Hardware RAID requires a controller to configure the RAID arrays.
- Hardware RAID has its own BIOS that comes with a special system setup to configure the RAID array.
- The completed array looks like a dingle drive to the operating system.
  Mass Storage Troubleshooting
- 1. Back it up! - Make a backup of whatever your working on before its too late or too expensive!.
- 2 – Mental Reinstall – If its a new device you just installed and its not doing what you want it to go through the installation steps mentally and make sure you did not forget anything.
- 3 – Triple check – Check everything twice and once more to make sure! A lot of times things not working comes from forgetting a simple step in configuration or installation.
- RAID not found / not working – Make sure that it was even installed. Make sure RAID is active, make sure you have the correct drivers for the specific system etc.
- Always back up important data before troubleshooting mass storage.
- Use a mental process of installation to make sure all the installation steps have taken place.
- Review the many symptoms in the episode!

Implementing Mass Storage Quiz
- What is the minimum number of drives to perform RAID 5?
- It takes a minimum of three drives to create a RAID 5 array.
- What is the maximum number of drive failures under RAID 6 at which the array will still function?
- A RAID 6 array will function with up to two drive failures.
- Which is an example of a hardware RAID controller?
- A dedicated RAID controller comes in the form of an expansion card. Storage Spaces is a Microsoft software RAID implementation. Dynamic and basic disks are not RAID controllers.
- RAID 10 requires how many drives?
- RAID 10 requires 4 drives.
- Which is most likely the result of a corrupted operating system?
- Of the choices here, the most likely result of a corrupt operating system is continuous reboots. Boot order is set in the UEFI/BIOS system setup utility. A corrupt OS can cause crashes and reboots, not slow performance. Hard drive clicking comes from a mechanical failure inside the hard drive.
  Section 11 Notes
  Chapter 10: Essential Peripherals
  Optical Media
- Compact discs (CDs) store 650-700 MB of data
- Digital video/versatile discs (DVDs) store from 4.37 GB to 15.9 GB
- Blu-ray Discs (Bds) store 25 GB to 50 GB
- All optical media comes in read only memory (ROM), write-once (R), and write-many (RW/RE) versions.
  USB Standards
- USB 1.0 – (1.5 Mbps)
- USB 1.1 – (12Mbps)
- USB 2.0 (480 Mbps)
- USB 3.0 – (5Gbps)
- USB 3.1 Gen1 – (5 Gbps)
- USB 3.1 Gen 2 (10 Gbps)
- Universal Serial Bus (USB) 1.1 comes in 1.5 Mbps and 12 Mbps; USB 2.0 runs at 480 Mbps
- USB 3.0 runs at 5 Gbps; USB 3.1 runs at 10 Gbps
- USB connectors often use colors to show versions
- USB connectors come in many types: Type-A, Type-B, Type-C, standard, mini. And micro.
  Understanding USB
- All USB devices connect to USB controllers built into the motherboard of the system; the USB controller is in charge of all connected USB devices.
- This creates an upstream/downstream concept.
- USB type-A connectors plug into downstream USB ports; USB Type-B connectors plug into upstream USB ports on peripherals.
  Configuring USB
- USB devices must have a device driver.
- Operating systems come with thousands of built-in device drivers.
- In some cases, you may need to download the correct driver for a USB device from the internet.
- You can disable USB ports through the system settings as well as use a USB lock.
  - Designed to watch over your USB ports. Not allow people to use USB ports but also whitelists things running on your USB ports.
  Thunder and Lightning
- Thunderbolt 1 – 10 Gbits/s (x2 channels)
- Thunderbolt 2 – 20 Gbits/s
- Thunderbolt 3 – 40 Gbits/s
- Lightning is exclusive to apple, proprietary.
- Thunderbolt is a general purpose I/O port that runs at 10 Gbps up to 40 Gbps.
- Thunderbolt uses a mini DisplayPort or a USB C connector.
- The lightning standard is exclusive to Apple products.
- Lightning uses a proprietary lightning connector.
  Keyboards and Mice
- KVM switch – (For keyboard, video, and mouse).
- Keyboards use either a USB or PS/2 connections
- Mice almost exclusively use USB
- Game controller often have a proprietary connection that requires a converter.
- Keyboard, video, mouse (KVM) switches enable multiple computers to share a single keyboard, monitor, and mouse.
  Sight and Sound
- Sound is commonly built into today’s systems.
- Speaker systems include satellites and subwoofers called 2.1 or 5.1 systems.
- Sound uses 3.5mm jacks or SPDIF
- Many devices, like webcams or headsets, include speakers.
  Readers and Scanners
- Smart card/magnetic readers are used to read cards.
- Flash memory readers read many types of flash memory.
- SD cards are very popular flash memory
- Scanners read paper documents. Automatic document feeders enable scanning multiple pages.
- Bar code and QR code scanners read printed coded labels.
  Using Expansion Cards
- Always handle expansion cards carefully, avoiding the contacts.
- Apply power, data connections or dongles as needed.
- Make sure to add the correct driver, check the Device Manager to confirm good drivers.
- A new device installation is a common place for Blue Screen of Death screens.
  Essential Peripherals Quiz
- Which is a valid capacity for a Compact Disc?
  - 74 minutes is a valid CD capacity. The other values are not valid for CDs.
- Which is not a valid USB speed?
- Each version of USB in a computer has its own what?
  - Each version of USB in a computer has its own USB controller which is then connected to a USB hub. USB Type-B connectors connect to a downstream peripheral (such as a printer). A USB hub is a circuit or device with one or more upstream USB ports. Each version of USB does not have its own peripheral.
- Most USB peripherals already have a what?
  - Windows comes with drivers for many common USB devices. A USB lock is an unpowered physical plug that secures open USB ports on a computer, not part of a USB peripheral. There is no such thing as an HID interface. USB devices come with USB connectors, not Lightning connectors.
- Which is not a valid Thunderbolt speed?
  - 30 Gbps is not a valid Thunderbolt speed. Thunderbolt 1 runs at 10 Gbps, Thunderbolt 2 runs at 20 Gbps, and Thunderbolt 3 runs at 40 Gbps.
- What color is a PS/2 mouse port?
  - PS/2 mouse ports are green. PS/2 keyboard ports are purple. Red and blue PS/2 ports are not a standard and are seldom, if ever, seen.
- Which utility would a technician use to configure mouse settings?
  - Control Panel is the usual utility to configure mouse settings. Mouse settings are not configurable in Display Settings or the Disk Management utility. Mice do have configurable settings.
- What kind of audio connector provides digital audio output?
  - S/PDIF is the Sony/Phillips Digital Interface. The other connector choices are all analog, not digital.
- Which is not a consideration when selecting a slot in which to install an expansion card?
  - The operating system has no bearing on which slot an expansion card is installed into. Air flow, type of slot, and room for rear connectors are all important considerations when selecting an expansion card slot.
- Which is not a step in installing a new expansion card?
  - The computer should be turned off before installing a new expansion card (and not be turned on until the installation is complete). All of the other choices are normal steps when installing a new expansion card.
  Section 12 Notes
- Building A PC
- Thick Client – Most basic desktop office system. Hardware the meets recommenced requirements for the OS you plan on running. Middle of the road gear. Basic setup to run desktop applications. MS office, etc.
- Thin Client – Rarely counts on its own internal storage. Relies on network connectivity. Meets minimum requirements for OS. Main difference between Thick and think client
- Graphic/CAD/CAM/Design workstation – Good multi core processor, powerful motherboard, high end video hardware.
- Virtualization workstation – Powerful system with lots of CPU cores and lots of RAM. High end motherboard etc. Depends on if system is running a number of virtual systems. Also needs plenty of storage.
- NAS – file sharing. This is what this system is all about. Gigabit NIC should be the minimum. RAID array to protect data. Don’t tax CPU much but it will be taxing the network. Need lots fo storage set up in a RAID array.
- Gaming PC – Nothing that taxes your system like gaming. Need multi-core processor with a motherboard that can support it. High end power supply along with high end cooling preferred. Specialized graphics card, even use multiple cards at once using SLI for high resolutions. High end sound cards recommended as well as good storage such as a large SSD.
- Audio/Video editing workstations – Similar to the gaming setup. Consider getting high end MACS for this job.
- Memorize details about each specialized system
- Consider different jobs and make sure the system matches the job specifications.
- Concentrate on RAM, storage, and graphic needs.
  Section 13 Notes
  Chapter 17: Display Technologies
- Monitor Technologies
- Pixel – Picture element.
  - Made up of three individual pieces that emit red green and blue light.
- A monitor is composed of individual picture elements (pixels); the total pixels across and down is the resolution.
- Liquid crystal display (LCD) monitors use liquid crystals to allow light to pass or not pass for each color in a pixel.
- LCD back lights are fluorescent or LED lights and shine through the liquid crystals
- Organic LED (OLED) doesn't use a back light, as pixels make their own lightning
- Digital Light Processing (DLP) uses a grid of tiny mirrors that shine through a color wheel to create a image.
- LCD Break Down
- Only CCFL screens need inverters
- Panel
  - Backlit unit – If CCFL then it has inverters to convert DC power to AC.
  - Connectors
  - Input from data
  - Power connection
- An LCD panel has a preset resolution.
- The back panel (backlit unit)
- Graphics Cards and Connections
- Nvidia, ATI/AMD, Intel (Intel designed to run off motherboard usually) make the majority of GPUs.
- VGA – Video Graphics Array.
- DVI – Digital Visual Interface.
- All graphics cards have RAM to help resolve the screen.
- Many CPUs come with built-in GPUs.
- VGA uses an analog signal; DVI uses a digital signal.
- Installing a Graphics Card
- Almost all graphics cards use 16-lane PCIe slots and one or two PCIe power connectors.
- With multiple graphics cards, define the primary card in system setup.
- Some systems provide riser cards for extra graphics cards.
- Always run the system at your monitor’s native resolution.
- Monitor Technologies Projectors
- DLP and LED projectors are the most common.
- Lumens – measurement of brightness. Different lumens for different projectors. Good for different situations.
- Projectors have resolutions and aspect rations just like monitors.
- Projectors usually have either DLP or LCD technology.
- Lumens define the brightness of the projector.
- When you move closer with a projector the image gets smaller, as you move back it gets larger. This is know as throw and projectors have a recommended throw distance.
- Make sure you understand throw, pincushion, keystone and skew.
- Monitor Technologies Troubleshooting Monitors
- Overheat shutdown
  - Video cards come with their own cooling built in. They also monitor themselves(turn on and off by themselves). Could mean you have bad fans on your video card.
  - Video card could be packed in to tight, lack of ventilation.
- Dead Pixels
  - Happens on LCD monitors. Manufactures actual have a set amount they allow.
  - If you have annoying dead pixels towards the middle that are black or maybe white chances are you have to return it and get the screen replaced.
- Artifacts
  - This is when something that was just displayed on the screen continues to linger to long afterward. Not some random image, it is something that was already displayed.
  - Your going to want to look at the video RAM itself. Unfortunately there is no real way to test it.
  - Try a different video card and run the same image. If it works, than previous video RAM is faulty.
  - No real replacement, they are all pretty much soldered on.
- Incorrect Color Patterns
  - First, check your cables. VGA cables are notorious for displaying weird colors when not properly inserted.
  - Once again it can be the video RAM, only real way to test is to try running another video card.
- Dim image
  - Was a bigger issue when using CCFLs. Older bulbs begin to fade down. Can replace bulbs.
- Flickering Image
  - Check the cables. Cables are notorious for a flickering image especially HDMI cables that are not really designed to be plugged in and out a lot. Double check your cables and make sure the cables pins and the inputs look good.
- Distorted Image
  - Make sure you are running at the native resolution of your monitor. A monitor not running at its native resolution is going to look weird and distorted and fuzzy. First thing you are going to want to check.
  - Happens with projectors all the time, it is a matter of adjusting your geometry a little.
- Burn in
  - Hardly happens. On plasma monitors you can get burn in. If you leave your screen on a certain image for a long time. Several technologies to fix it.
  - With LCD’s you can get burn in but its called image persistence. Change the image regularly and it goes away.
- Over-sized images and icons.
  - Adjust text size within windows display settings. Usually happens when jumping around different resolutions or settings are messed with.
- CompTIA exams cover many monitor troubleshooting situations.
- All these situations above are on the exam.
- Monitor Technologies Display Technologies Quiz
- Section 14 Notes
  Chapter 18: Essentials Of Networking
  Introduction to Networking
- Ethernet -
- Frame -
- Mac Address – Media access control (MAC) address ( Ex. 00-14-22-01-23-45). Every network card gets a unique mac address.
  - First 6 characters are the OEM id.
  - Ipconfig /all shows IP info including your network cards mac address within the command line on a windows system.
  - Ifconfig on mac OS systems.
- Every time we send of a frame it is set up with other information aside from the data.
  - -Destination MAC address – Source Mac Address – Data – FCS Frame Check Sequence.
    - Frame Check Sequence checks data, gives a good idea if data cae in good order.
- IP address’s are not very important in a small LAN. Matter more in WAN.
- LAN computers connect with ethernet.
- Ethernet frames standardized as 1500 bytes.
- A MAC address uniquely identifies a host on a LAN.
- Use ipconfig (Windows) or ifconfig (Linux) to view MAC.
  Hubs vs. Switches
- Hubs are known as repeaters.
  - If a computer on the LAN sends a message to another computer through the hub, all connected computers receive the message but unintended recipients delete after checking the MAC address within the frame and confirm it is not for them.
- As a computer connects to a switch, the switch takes note of the MAC addresses of the connected computers and adds them to a list.
  - As a frame goes through a switch it reads the destination MAC address and sends it to the intended recipient (unlike Hubs which repeat the frame to everyone).
  - Switches work a lot better than hubs. Nobody uses hubs anymore, surprisingly hubs are still on the compTIA exam.
  - Hubs repeats back on all ports. Switches are still a repeater, but it is a smart repeater. It checks the destination MAC address and sends it only to the computer on that port.
- Hubs repeat all traffic on the LAN to all nodes.
- Switches filter traffic based on MAC address.
- Switches provide full bandwidth for all nodes.
  Hexadecimal
- Notice when you check a MAC address its all numbers and letters that don’t pass F. These letters are hexadecimals.
  - Hexadecimals – complete base 16 number system.
  - Point of hexadecimal is to avoid having to right long strings of 1’s and 0’s, and compress that a lot into smaller values.
- Every hexadecimal is 4 binary values.
  - 40-8D-5C-1C–5A-0-50. 4 x 12 = 48 bit address.
  - Used as a shorthand to represent long strings of binary values. Write ¼ as many things on the screen essentially.
- Hexadecimal (base 16) enables discussion of long strings of 1s and 0s.
- Each hex character represents 4 binary numbers (0000-1111)
- in hex, numbering goes 0-9, a-f, for 0-15.
  WANs and Routers
- Daisy chained switches act as 1 switch essentially.
- Instead of one huge LAN it is better to break computers into several small LANS (30-40 computers) and connect to a WAN (Wide Area Network).
- If a MAC address is a physical address (burned into the device at the factory), a logical address is something set when established with your LAN. You configure and type this in.
- The same way switches remember MAC addresses routers remember logical addresses. We have to type this in and configure this. Tell it which computers are under what LAN.
- DHCP in a sense auto configures computers that connect.
- Every computer has a physical (MAC) address for local calls, then a logical address based on IP addressing.
- Switches connect (up to 1024) computers in a LAN.
- Routers connect multiple LANs together in a WAN.
- Routers use logical addressing (IP addressing) to determine local vs remote traffic.
  Cables and Connectors
- Coaxial RG ratings = RG-58, RG-59, RG-6
  - RG-6 = F type connector
  - RG – 58 = Thin coaxial cable, uses BNC.
- Predominant cable is twisted pair.
  - No metallic foil? - UTP – Unshielded twisted pair.
  - UTP – run at about 100M – distance between switch and computers.
- RJ – 11 = Used for telephones – 4 contacts
- RJ – 45 = Has 8 contacts
- STP – Shielded twisted pair – still RJ-45 but is shielded throughout the wire. This provides protection from interference.
- Electric motors and florescent lights mess with UTPs whereas STP is more protected.
- Fiber optics use light and not electricity. Used for faster speeds.
  - Multimode – uses Leds – tend to be found in networking environments.
  - Single mode – uses lasers
- Fiber optic wires either send or receive.
  - Uses 2 wires, one for each.
- Cat Ratings – rating given to cables to describe how much more information they can handle.
  - Cat 5 = cat5e
  - Cat 6 = 1Gbps (up to 100m) – 10Gbps (55m)
  - Cat 6a = 10 Gbps at 100m.
- Plenum ratings – fire resistance rating given to wires made for use in a plenum.
  - Plenum = space between drop ceiling and the actual ceiling (where cables are ran).
  - PVC = non plenum, most flammable.
  - Plenum rating = Most fire resistant.
  - Riser Rating = used between floors. More flame resistant that PVC but less flame resistant than plenum rated.
- Coazial cables use RG ratings and F-type connectors.
- Most networks use twisted pair cabling.
- Fiber optic cable use light, rather than electrical pulses.
- Twisted pair cabling have different category (Cat) ratings.
  Crimping Cables
- ,
  Structured Cabling
- .
  Apparently
  Section 15 Notes
  Section 16 Notes
  Section 17 Notes
  Section 18 Notes
  Section 19 Notes
  Section 20 Notes
  Section 21 Notes
  Section 22 Notes
  Section 23 Notes